3.3V Current Demand Verification:

3V3 Regulator P/N: MCP1725-3302E/SN
Maximum Current: 500 mA
Dropout: 210 mV (typical)
Input Voltage Range: 3.51 – 6.0 V

3V3 Devices and maximum current

PIC18F45J10	250 mA (absolute max per datasheet)
1206 SMT LEDs	25 mA (x6) (maximum source current)
U501 GPS Receiver	38.33 mA (maximum search mode)
MiWi	23 mA (maximum transmit power)
Total	461.3 mA
Available Current	500 mA
Current Margin	38.7 mA

Note: PCA9600 VCC is driven by 5V I2C bus power

3V3 Regulator Circuit Verification:

Section 4.4 of MCP1725 calls for an input capacitor of at least 1.0-4.7 uF.

For resilience against transients when using the board in an I2C bus powered mode, 10 uF capacitors were selected (as shown in figure 5-1 on datasheet).

PCA9600 Bias Circuit Verification:

The discrete components used for the PCA9600 active terminator were chosen from the datasheet:

With values chosen from the following table (line three):

Xtal Oscillator Capacitor Loading Verification:

Part Number: ECS-200-18-4XEN

This requires 18 pF in parallel across the crystal oscillator. Therefore each capacitor should be 9pF.

Device Pinout Verification:

3V3 Regulator:

MiWi Module:

PCA9600 Active Terminator

5V Regulator Pinout:

Part Number: L78S05CV

Datasheet Recommended Capacitors:

Confirming physical layout of 5V Regulator:

On the actual PCB (from left to right, 5V, VSS, REGULATORS)

PIC18F45J10 Pinout verification

GPS Pinout Verification:

PICKIT Pinout Verification: